## Slide 1
BENCHMARK REPORT · 2026
SUSTAINABLE
RAW MATERIAL
BENCHMARKING
Best Practices, Decision Framework & Analytics Prototype
A decision method demonstrated on synthetic data.
No supplier, company or market data is used or implied.
ELIGIBILITY · COMPARABILITY · TRADE-OFF
25 material alternatives · five benchmark cases
green improves on cost, red deteriorates · synthetic
Sustainable Raw Material Benchmarking · Design pilot · v0.1 · Csaba Bakay

## Slide 2
I THE MANAGEMENT PROBLEM
No raw material is universally sustainable — a defensible decision
proves eligibility, then comparability, then shows the trade-off
Sourcing decisions fail in three specific ways. The answer is not a better score; it is a sequence that makes each failure mode visible before the next one is judged.
GHG Protocol Product Life Cycle Accounting and Reporting Standard (WRI/WBCSD, 2011), §1.5 and Appendix A · European Commission JRC, Environmental and economic assessment of plastic waste recycling, JRC132067 (2023). The three failure modes are a project synthesis of these sources.
1
01
ELIGIBILITY
Can this alternative be considered at all?
Failure An option is compared that cannot legally or technically be bought.
Control Screen on true constraints first — and keep what was screened out visible.
›
02
COMPARABILITY
Were these numbers ever comparable?
Failure Two figures are compared that were never calculated on the same basis.
Control Prove equivalent function, boundary, allocation, period and assurance.
›
03
TRADE-OFF
What are we giving up, and who owns that call?
Failure One dimension improves while another quietly moves the wrong way.
Control Hold the dimensions on separate axes and name the decision owner.
Each control is demonstrated later on the prototype: eligibility on page 10 · comparability on page 11 · trade-off on pages 9 and 13

## Slide 3
I THE MANAGEMENT PROBLEM
Carbon is the dimension we measure best — and the carbon
standard itself says it is not the whole answer
A product carbon footprint is decision-relevant and, in the chemical context, unusually well supported by supplier-exchange infrastructure. It is still one impact category.
Quotation: GHG Protocol Product Life Cycle Accounting and Reporting Standard (WRI/WBCSD, 2011), §1.7, read in the original; emphasis added. · Methods for other dimensions: ISO 14046:2014 (product water footprint); Commission Recommendation (EU) 2021/2279, Product Environmental Footprint, 16 impact categories. · The data-availability constraint is a source-supported interpretation.
2
“The limitation of a GHG-only inventory is that potential trade-offs or co-benefits between environmental impacts can be missed. Therefore, the results of a GHG-only inventory should not be used to communicate the overall environmental performance of a product.”
GHG Protocol Product Standard, §1.7 — Limitations of product GHG inventories
What the number covers
Climate change one impact category
Cradle-to-gate a partial life cycle
kg CO₂e per kg a declared unit, not a function
What it is silent on — named by the standard itself
Ecosystem degradation
Resource depletion
Ozone depletion
Negative human health impacts
And methods exist for the rest
ISO 14046 product water footprint
EU PEF 16 impact categories
The binding constraint is comparable supplier data, not the absence of a method.

## Slide 4
I THE MANAGEMENT PROBLEM
Which dimensions matter depends on the material, its feedstock
and its origin — not on a universal checklist
A universal ESG data request produces effort, not decisions. The constant is the screening question; the answer changes with what is bought, what it is made from and where it comes from.
Classification and drivers: author synthesis, built on ISO 14046:2014, Commission Recommendation (EU) 2021/2279 (PEFCRs fix relevant impact categories per product group), Regulation (EU) 2024/1252 and Directive (EU) 2026/470. · The classification is a project synthesis on sourced dimension definitions. · Supplier-level social performance data is class E — currently insufficiently measurable.
3
The screening question Could this dimension materially change the decision for this material, from this feedstock, from this origin?
DECISION DIMENSION
CLASS
MATERIAL
FEEDSTOCK
ORIGIN
APPLICATION
Climate / GHG — product carbon footprint
A
Technical performance and qualification
C
Specific legal compliance
C
Commercial performance — price, TCO
A
Circularity / resource loops
B
Pollution / toxicity
B
Water
B
Resource use
B
Supply-chain resilience
B
Land use / biodiversity
D
A core
B context-dependent
C gate / compliance
D big picture, not this prototype
driver that can change materiality

## Slide 5
II WHAT BEST PRACTICE LOOKS LIKE
Most things called “gates” are not gates — and mixing the four
decision roles is what breaks a benchmark
Four dimensions can look alike on a data sheet and behave completely differently in a decision. A gate is not a preference, and evidence is not performance.
Decision-role convention: project synthesis · C6 Ashby, constraints vs. objectives · A2 ISO 14044 and P3 PACT v3 for evidence metadata · V2 REACH Annex XIV / XVII instruments · V1 Directive (EU) 2026/470, applying from 26 July 2029 to a narrow set of very large companies. The four-role convention is a PROJECT SYNTHESIS; the legal statements are fact.
4
PROJECT SYNTHESIS a practical decision convention, not a validated external framework
GATE
Can this alternative be considered at all?
Pass / fail.
Never traded off.
PERFORMANCE
How does an eligible alternative perform?
Compared, plotted,
traded off.
EVIDENCE
How much confidence does that comparison deserve?
Reported beside the number,
never blended into it.
CONTEXT
Under what material, application and supply conditions?
Filters and explains.
Not optimised.
A gate without a named threshold owner is an opinion. Every gate names its threshold owner, decision owner and time horizon.
THE ROLE IS SET BY THE DECISION RULE, NOT THE TOPIC NAME
Supply risk — gate where a minimum volume or dual-source policy is contractual; performance where lower concentration is preferred; context elsewhere
Regulatory criteria — gate only where the specific use is unlawful, unauthorised or outside written company policy — disclosure duties are not gates
Social criteria — gate for prohibited conduct or an explicit minimum requirement; general due diligence is a risk-based process, not a certificate
WHAT IS — AND IS NOT — A GATE
Not a gate
REACH Candidate-List presence a disclosure duty
General due diligence status a risk-based process
A gate
Annex XIV after sunset, without authorisation
Annex XVII restriction covering the specific use
An explicit company policy threshold

## Slide 6
II WHAT BEST PRACTICE LOOKS LIKE · BEST-PRACTICE ANCHOR
Screen, compare, qualify, decide, record — the practices that
survive the evidence, and how strongly each is supported
Thirteen practices came out of the research. Four are strongly evidenced. Showing which is which is itself a practice — it stops a plausible recommendation being read as an established one.
BP-1 to BP-13: author synthesis, with the evidence recorded for each practice · P1 GHG Protocol Product Standard §A.1 · P2 JRC132067 · P3 PACT v3 · A1 ISO 20400 · A2 ISO 14044. The marker describes how well a practice is supported — never organisational maturity. No scoring, no ranking, no maturity model.
5
SCREEN
eligibility
›
BP-1
Screen on hard constraints first
BP-9
Gate on specific legal thresholds, not general risk
BP-8
Treat supply risk as a dimension, not a footnote
COMPARE
comparability
›
BP-13
Define equivalent function before any per-kg benchmark
BP-5
Satisfy the six comparability conditions first
BP-2
Require the primary-data share, not just a figure
BP-12
Declare a comparability verdict, not a colour
QUALIFY
evidence
›
BP-3
Carry evidence quality beside the number, never inside it
BP-4
Never substitute zero for missing data
DECIDE
trade-off
›
BP-6
Decide on total cost, not on price per kg
BP-10
Price in regulatory cost transmission early
BP-7
Validate circularity against life-cycle impact
RECORD
owned
BP-11
One decision record, not two
Shared by procurement and engineering, with the gate reasons visible.
strongly evidenced — primary standard or EU authority
supported — cited, but narrower
project recommendation — plausible, not externally evidenced
What a procurement organisation does differently
Name the rulebook in the RFQ · report the primary-data share · keep evidence beside the number · never zero-fill a gap · one decision record, not two

## Slide 7
II WHAT BEST PRACTICE LOOKS LIKE
Two supplier carbon footprints are not comparable until six
conditions hold — and a PCF alone satisfies none of them
The standard that defines the product carbon footprint also states that it does not, on its own, support a purchasing comparison. Comparability is engineered upstream in the specification.
All six conditions verbatim from the GHG Protocol Product Life Cycle Accounting and Reporting Standard (WRI/WBCSD, 2011), Appendix A §A.1; Table A.2 states that business purchasing decisions are not supported by the standard unaided. · D1 BASF disclosure of economic allocation where physical data is unavailable. · B1 TfS, B3 Catena-X and P3 PACT v3 are examples of the additional programme specifications §A.1 requires; conformance to them was not verified here. The three-state verdict is a source-supported interpretation.
6
SUPPLIER A
Product carbon footprint, kg CO₂e per kg
SUPPLIER B
Product carbon footprint, kg CO₂e per kg
A PCF alone satisfies none of the six conditions.
THE SIX CONDITIONS FOR A BUSINESS PURCHASING COMPARISON
GHG Protocol Product Standard, Appendix A §A.1 — verbatim
1
The unit of analysis is identical
2
System boundaries and the temporal boundary are equivalent
3
The same allocation methods are used for similar processes
Broken between two honest suppliers wherever one allocates economically and the other physically.
4
Data types, data quality and uncertainty are reported and assessed
5
Temporal and geographical representativeness is assessed
6
Third-party assurance has been performed
The least met of the six in practice.
Comparable
Conditionally comparable
Not comparable
Where the methodological gap could plausibly exceed the measured difference, report no difference.
The prototype does not yet demonstrate compliance with these conditions — page 12 names the fields that would close it.

## Slide 8
II WHAT BEST PRACTICE LOOKS LIKE
A number without its evidence is not a measurement — and a
missing number is never a zero
Evidence is four separate things, and none of them may be folded into the performance number. If absence defaults to zero, the least transparent supplier becomes the best performer.
P3 PACT v3 reliability KPIs, incl. share of primary data · A2 ISO 14044 temporal, geographical and technological representativeness · P1 GHG Protocol Product Standard §A.1, conditions 4 and 6 · P2 JRC132067, mixed primary-foreground / secondary-background inventory structure · E2. The four-way split of evidence is a source-supported interpretation. The value shown is illustrative and is not taken from the dataset.
7
BARE
2.4 kg CO₂e / kg
Provenance ?
Data quality ?
Verification ?
Uncertainty ?
A number. Not a measurement.
QUALIFIED
2.4 kg CO₂e / kg
Provenance supplier-specific; primary-data share
Data quality temporal, geographical, technological
Verification third-party assurance performed
Uncertainty assessed and reported with the value
The same number, now usable.
ABSENT
—
no figure reported
0
never
If absence defaults to zero, the least transparent supplier becomes the best performer.
Missing stays missing.
Supplier-specific is not the same as primary. A supplier-specific footprint normally combines primary activity data with secondary background factors — which is why PACT reports a share of primary data, not a flag.
Carried into the prototype. It implements provenance and temporal quality, and enforces the never-zero rule at four independent layers — page 8.

## Slide 9
III FROM PRINCIPLE TO ANALYTICS
A working demonstrator on synthetic data — where the portfolio
total is five times smaller than it first appears
Five benchmark cases, twenty-five material alternatives, one incumbent in each. The demonstrator carries the decision structure end to end — and its first lesson is an arithmetic one.
SYNTHETIC DEMONSTRATION DATA — no supplier, company or market data is used or implied. · Figures computed from data/processed/consolidated_material_benchmark.csv through the 21 audited semantic measures; percentage deltas are recomputed from absolute values per audit item A3.
8
SYNTHETIC DEMONSTRATION DATA
PORTFOLIO POSITION
All 25 options, summed
4,073,400 €
Every alternative is a scenario for the same demand. Summing them counts that demand five times over.
The incumbent portfolio — the position actually held
820,000 €
480,000 kg annual volume 605,000 kg annual CO₂e
THE DEMONSTRATOR
CASE-A
Base Oils
1 incumbent · 4 alternatives
CASE-B
Solvents
1 incumbent · 4 alternatives
CASE-C
Surfactants
1 incumbent · 4 alternatives
CASE-D
Polymer Additives
1 incumbent · 4 alternatives
CASE-E
Resins / Binders
1 incumbent · 4 alternatives
COVERAGE ACROSS ALL 25
23 / 25
technically eligible
92.0%
24 / 25
PCF available
96.0%
96.8%
of spend covered by a PCF
What the demonstrator shows
The decision structure end to end: gates that screen without deleting, evidence carried beside performance, and every missing value preserved as missing.
What it does not show
A validated supplier comparison. No conformance to the six §A.1 conditions is claimed, and no real supplier, market or company data is used — page 12 states exactly what is absent.

## Slide 10
III FROM PRINCIPLE TO ANALYTICS
SYNTHETIC DEMONSTRATION DATA
All 25 alternatives on one surface: cost and carbon as the
analysis, technical and evidence status as exceptions
improvement against the incumbent of the same case
deterioration, or a technical blocker
weak, outdated or missing PCF evidence
incumbent, or normal state
SYNTHETIC DEMONSTRATION DATA. Report-native re-render of the Power BI Python visual (powerbi/…/visuals/99aabbccddeeff001122) — plotting logic reused verbatim; only the figure size and the chrome now supplied by this page differ. · Deltas are computed against the incumbent of each case from absolute spend and CO₂e. · n / a is unknown and is never read as zero · ▸ marks the incumbent · each case is an independent decision · no score, no ranking, no weighting.
9

## Slide 11
III FROM PRINCIPLE TO ANALYTICS · CASE-D POLYMER ADDITIVES
The two strongest alternatives in this case
are the two you cannot currently buy
On cost and carbon the answer looks obvious. On eligibility, two of the five are not purchasable — and no performance number changes that.
SYNTHETIC DEMONSTRATION DATA. CASE-D, all five materials, from the governed dataset via the audited measures. · Eligibility is the prototype gate (technically_eligible, technical_approval_status); it is shown, never used to filter rows away — BP-1. · Screening removes an option from the comparison, not from the record.
10
SYNTHETIC DEMONSTRATION DATA
better on both
Cost delta % vs incumbent cheaper ← → dearer
CO₂e delta % vs incumbent lower carbon ↓
PA-4001
PA-4002
PA-4003
PA-4004
PA-4005
blocked
blocked
EVERY OPTION STAYS ON THE RECORD
COST Δ
CO₂E Δ
TECHNICAL STATUS
PA-4001
0.00%
0.00%
Incumbent
PA-4002
−14.29%
−38.89%
Not Approved
PA-4003
−3.57%
−5.56%
Approved
PA-4004
−7.14%
−16.67%
Under Qualification
PA-4005
+3.57%
+8.33%
Approved
The only eligible improver is PA-4003 — −3.57% cost and −5.56% CO₂e. That, not −14.29%, is the decision actually on the table.
PA-4004 is under qualification and may return. Both blocked options stay visible, with the reason attached.
Performance cannot compensate for failed eligibility. A gate is passed or it is not; it is never traded off against a better number — page 4.

## Slide 12
III FROM PRINCIPLE TO ANALYTICS · CASE-C SURFACTANTS
The best carbon result rests on the weakest evidence — and
one material has no carbon figure at all
All five are technically approved, so eligibility decides nothing here. Evidence decides everything — and the two are read in different columns.
SYNTHETIC DEMONSTRATION DATA. CASE-C, all five materials, from the governed dataset via the audited measures. · BP-2 an industry-average factor cannot distinguish two suppliers within the same industry · BP-3 evidence quality is carried beside the number · BP-4 missing is never zero · P3 PACT v3 · A2 ISO 14044.
11
SYNTHETIC DEMONSTRATION DATA
MATERIAL
COST Δ %
CO₂E Δ %
PCF KG CO₂E / KG
PCF DATA TYPE
YEAR
CONFIDENCE
SF-3001
0.00%
0.00%
2.10
Supplier-specific (primary)
2023
High confidence
SF-3002
+6.25%
−54.76%
0.95
Industry-average (secondary)
2019
Low confidence
SF-3003
−8.33%
no PCF reported
No data
SF-3004
+10.42%
−23.81%
1.60
Supplier-specific (primary)
2023
High confidence
SF-3005
−2.08%
+7.14%
2.25
Supplier-specific (primary)
2023
High confidence
SF-3002 — the strongest carbon result in the case
−54.76% CO₂e, carried by the weakest evidence on the page: an industry-average factor from 2019, low confidence. An industry-average factor cannot distinguish two suppliers within the same industry. The number is not wrong — it is not yet a supplier comparison.
SF-3003 — no carbon figure at all
−8.33% on cost, and blank on carbon everywhere: in the measure, in the heatmap, in the case total. It is not zero, it is not a worse performer, and it is not dropped from the cost comparison. It is unknown, and it stays unknown.
The result and the confidence in the result are two columns. Blending them into one figure destroys both — page 7.

## Slide 13
III FROM PRINCIPLE TO ANALYTICS
The architecture is right; the comparison is not yet demonstrably
valid — and we know which fields would close it
Page 6 set six conditions. Measured against them the demonstrator is honest about what it cannot yet support — which is exactly what makes it usable as a specification.
SYNTHETIC DEMONSTRATION DATA. Conditions verbatim from the GHG Protocol Product Standard, Appendix A §A.1. · Prototype status assessed against the fields present in the semantic model. · No condition is fully satisfied today, so no status on this page is green. · The closing fields are the prototype v0.2 candidate list.
12
SYNTHETIC DEMONSTRATION DATA
CONDITION — GHG PROTOCOL §A.1
IN THE PROTOTYPE TODAY
STATUS
THE FIELD THAT WOULD CLOSE IT
1
The unit of analysis is identical
A per-kg declared unit only
partial
Functional or declared unit, with the reference flow
2
System and temporal boundaries are equivalent
No boundary or data-period field
not shown
Cradle-to-gate boundary flag; data period
3
The same allocation methods are used
No rulebook or version recorded
not shown
Rulebook and version — TfS, PACT, Catena-X
4
Data types, quality and uncertainty are reported
pcf_data_type, pcf_data_quality_tier
partial
Primary-data share; uncertainty range
5
Temporal and geographical representativeness
pcf_reference_year — temporal only
partial
Geographical representativeness
6
Third-party assurance has been performed
No verification field at all
not shown
Verification status and assurance level
What the demonstrator does establish
Gates that screen without deleting, evidence carried beside performance, missing values preserved, and each case kept as a separate decision.
Closing the six conditions is a data task, not a redesign
Every field in the right-hand column is collected upstream, in the specification and the RFQ. That scope is page 16.

## Slide 14
IV BEYOND CARBON
More circular is not automatically more sustainable — an EU
assessment shows exactly where recovery loses
Across 27 recycling pathways and 14 impact categories, recycling beat energy recovery on climate in every pathway analysed. On five other categories, energy-intensive routes lose.
European Commission JRC, Environmental and economic assessment of plastic waste recycling, JRC132067 (2023) — executive summary read in the original; quoted wording retained. · Supporting: C1 on recycling energy intensity. · FACT, within the stated scope. · The prototype does not measure circularity; nothing on this page comes from it.
13
Scope This is a plastics waste-treatment study. It demonstrates the mechanism — burden shifting between impact categories — and is not evidence about base oils, solvents, surfactants, polymer additives or resins.
CLIMATE
Recycling beat energy recovery in every one of the 27 pathways analysed. This is the finding a circularity target is usually built on.
WHERE ENERGY RECOVERY CAN PERFORM BETTER — FIVE OF THE FOURTEEN CATEGORIES
Acidification
Particulate matter
Ionising radiation
Human toxicity, non-cancer
Eutrophication
…for these energy-intensive recycling routes, named in the assessment
PET alkaline hydrolysis
PS mechanical
MPO mechanical & pyrolysis
PE film mechanical & physical
EPS physical
Three further findings from the same assessment
Technical quality issues in the recovered material · negative net incomes for methanolysis, pyrolysis and gasification · and, across the whole study, “a clear ranking could not be established”.
And the answer has a date on it
The assessment attributes the result to the European energy mix, and states that as the mix gets cleaner the gap will widen further in favour of recycling.

## Slide 15
IV BEYOND CARBON
Every trade-off has its own handling rule — and none of
them is a weight
The tensions are structurally different. Some resolve at a gate, some are genuine two-axis trade-offs, one is about evidence rather than performance. Not one of them needs a weighting.
T-1 to T-9: author synthesis, with the confidence recorded for each tension · P2 JRC132067 “a clear ranking could not be established” · P1 GHG Protocol Product Standard §1.7 on burden shifting · V3 ISO 14046, V4 EU PEF · BP-7. The map is a source-supported interpretation; the individual evidence items are fact. · Cost ↔ carbon quantitative figures in the register are steel-sector illustration only; no chemical-sector green-premium dataset was found in either research pass.
14
TENSION
HOW IT SHOWS UP
EVIDENCE
HANDLING RULE
Cost ↔ carbon
The cheaper option carries more carbon, or the reverse
Two axes, plus a displayed cost-per-tonne ratio — never a score
Circularity ↔ non-climate impacts
Recovery wins on climate and loses elsewhere
Report as distinct outputs; any priority rule is stated per case
Circularity ↔ technical performance
Recycled content shifts the specification
Gate — recycled content is a candidate only if it passes equivalence
Circularity ↔ cost
The break-even arrives later than the target date
Treat the horizon as an explicit scenario, not an assumption
Sustainability ↔ technical performance
A carbon gain sits behind a failed approval
Gate. No carbon result buys past a technical blocker
Sustainability ↔ supply security
A carbon gain raises supplier concentration
State it beside the result; concentration needs awarded volumes
Performance ↔ evidence quality
The best number has the weakest provenance
Two columns. Never a quality-adjusted performance figure
Carbon ↔ other environmental burdens
A GHG-only view misses the shift
Disclose scope. Methods exist — the constraint is supplier data
strongly evidenced — primary standard or EU authority
supported — cited, but narrower
project recommendation — plausible, not externally evidenced
Deliberately rejected
A composite sustainability score · arbitrary weighting · cross-case ranking of non-substitutable materials. An EU authority reached the same conclusion in its own domain: “a clear ranking could not be established”.

## Slide 16
V MANAGEMENT IMPLICATIONS
Four functions, one decision record, and a named owner
for every threshold
Every practice in this report fails at the same seam: gates, commercial comparison and evidence rules sit with different functions, and each keeps its own list.
A1 ISO 20400 places sustainability criteria alongside price and quality in a single evaluation rather than in a parallel process · BP-11: one comparison case, one decision record. The ownership split and the record's field list are a PROJECT SYNTHESIS and a design recommendation: ISO 20400 supports the principle, it does not validate this artefact.
15
PROJECT SYNTHESIS · DESIGN RECOMMENDATION
WHO OWNS WHICH DECISION
Engineering
Defines the function and validates technical equivalence
Procurement
Commercial terms, capacity evidence, sourcing scenarios
Sustainability
Accepted methods and evidence requirements
Compliance
Specific legal and policy gates; the due-diligence risk process
Suppliers
Provide declarations and evidence — never self-approve gate status
Business decision owner
Accepts the residual trade-off, on the record
ONE DECISION RECORD PER BENCHMARK CASE
Incumbent and candidates
the case, not the catalogue
Gate status, with the reason
blocked options stay visible
Cost position · carbon position
two axes, never merged
Evidence status per number
provenance, quality, verification, uncertainty
Comparability verdict
comparable / conditional / not comparable
The decision
and what was given up
Named owner
a threshold without one is an opinion
Review date
the record expires
A second output, not a footnote: the qualification pipeline. Which blocked candidates are worth qualifying, by when, and at whose cost.
The prototype is not yet this artefact. Power BI page 2 is the closest thing that exists: it displays the decision context, but it does not capture the decision, the owner or the review date.

## Slide 17
V MANAGEMENT IMPLICATIONS
Two lanes to build, one list to refuse — and the gaps we
are not pretending to have closed
Lane A makes the comparison already being made defensible. Lane B adds category modules where materiality justifies them. The third list is what must never be synthesised.
Categories 1–4 and the two lanes: project synthesis · limitations disclosed and not closed · Lane A derives entirely from GHG Protocol Product Standard §A.1. PROJECT SYNTHESIS, anchored on the frozen classification.
16
Build now — Lane A
makes the existing comparison defensible
Functional / declared unit and dosage normalisation
Methodology rulebook and version
Boundary description or comparability flag
Primary-data share (%)
Verification status and scope
Data / reference period
Uncertainty, or an uncertainty description
Comparable / conditional / not comparable verdict
All eight derive from GHG Protocol §A.1 — the conditions set out on page 12.
Build where material — Lane B
only where the decision can change
Recycled and renewable content, circularity
Due diligence and human-rights performance
Hazardous-substance legal status
Criticality and supply resilience
Water, land use, biodiversity, pollution, toxicity
CBAM exposure where the product code is out of scope
Each gated by the materiality screen on page 3, with its own data owner and grain.
Do not build
not until real data exists
Qualification and switching cost
True TCO effects on yield, energy, quality, downtime
Supplier capacity, ramp-up, allocation, recovery time
Country / supplier concentration on awarded shares
Toxicity, exposure and legal use status for real substances
Recycled / renewable chain of custody and mass balance
Responsible-sourcing findings and traceability depth
Synthesising any of these would demonstrate columns, not capability.
Research limitations — disclosed, not closed
No industrial chemical-procurement case · no empirical study of how far real supplier PCFs diverge when the six conditions are violated · TfS v3 and Catena-X v4 not read in full · no company-level resilience metric set · no chemical-sector green-premium dataset.
Implementation prerequisites — not defects in the method
Every Lane A field is collected upstream, in the specification and the RFQ. Comparability is engineered there — it cannot be repaired downstream in the analysis.